## Slide 1: Presentation on RC5
Presented By:- Mayank Kumar Jha
College:- Saroj Mohan Institute of Technology
Stream:- Computer Science and Engineering
Paper:- Cryptography and Network Security
Paper Code:-CS801D
Year:- 4th
Semester:- 8th
Roll:- 16800116066
Reg. No.:- 161680110031

## Slide 2: What is RC5
RC5 is a block cipher notable for its simplicity. Designed by Ronald Rivest in 1994.
RC stands for "Rivest Cipher", or alternatively, "Ron's Code.
Rivest announced also RC2 and RC4 and now there is RC6 which is The Advanced Encryption Standard (AES) candidate (RC6 was based on RC5).

## Slide 3: Features
Symmetric block cipher (Like Feistel Network Structure)
  the same secret cryptographic key is used for encryption and decryption
Suitable for hardware and software
  It uses only computational primitive operations commonly found on typical microprocessors
Fast
  Cause it uses Word-Oriented operations

## Slide 4: Features count.
Adaptable to processors of different word lengths
  For example with 64 bit processor RC5 can exploit their longer work length
  Therefore the number w of bits in a word is a parameter of RC5, different choices of this parameter results different algorithms.
Variable number of rounds
  The user can explicitly manipulate the trade-off between higher speed and higher security.
  So the number of rounds i is a second parameter of RC5

## Slide 5: Features count.
Variable length cryptographic key
  The user can choose the level of security appropriate for his application the key length b in bytes is thus a third parameter of RC5
Simple
  It is simple to implement, This simplicity makes it more interesting to analyze and evaluate, so that the cryptographic strength can be more rapidly determined
Low memory requirements
  So it is easily implemented on devices with restricted memory

## Slide 6: Features count.
Data-dependent rotations
 RC5 highlight the use of data-dependent rotations and encourage the assessment of the cryptographic strength data-dependent can provide

## Slide 7: Parameterization

## Slide 8: Parameterization count.
RC5 algorithm example: RC5-32/16/7
  similar to DES
  Two 32-bit word inputs and outputs
  16 rounds
  7-byte(56-bit) secret key
Choices for w and r
  speed vs. security
Choosing larger number of rounds provides an increased level of security

## Slide 9: Dropped parameters
RC5 Dropped parameters
  The default is 32/12/ 7 for 32 bit words
  The default is 64/16/7 for 64 bit words
  So if any parameter is dropped use the corresponding default parameter
Examples
 RC5-32 | Means | 32/12/7
 RC5-32, 9 | Means | 32/9/ 7
 RC5-64 | Means | 64/16/7

## Slide 10: Notations and Primitive operations

## Slide 11: Algorithm
The are three components of RC5
  Key expansion algorithm
  Encryption algorithm
  Decryption algorithm
Key Expansion Algorithm
Decryption Algorithm
Encryption Algorithm
Plaintext
Ciphertext
Plaintext
Ciphertext
Expanded Key S
Secret Key K

## Slide 12: Encryption

## Slide 13: Encryption
A = | A | + | S[0];
B = | B | + | S[1];
for | i A | = = | 1 to r do ((A ⊕ B)
<<< B) + S[2*i];
B = ((B ⊕ A) <<< A) + S[2*i + 1];
A <<< B
Bits in A are rotated to left by the amount specified by lower log2(w) bits in B

## Slide 14: Decryption

## Slide 15: Decryption
for | i | = | r downto 1 do | 
 | B | = | ((B - S[2*i +1]) >>> | A) ⊕ A;
 | A | = | ((A - S[2*i]) >>> B) | ⊕ B;
B = | B | - | S[1]; | 
A = | A | - | S[0]; | 
A >>> B
Bits in A are rotated to right by the amount specified by lower log2(w) bits in B

## Slide 16: Encryption and Decryption

## Slide 17: Key Expansion
RC5 performs some operations on the secret key to generate a total of t sub keys, which are stored in S array, S[0],S[1], …, S[t-1]
The key expansion algorithm consists of two constants (Magic numbers) and three simple algorithm parts
  Step-1: Convert secret key bytes to words
  Step-2: Initialize sub key array S (S[0], S[1], …, S[t-1])
  Step-3: Mix the secret key into sub key array S
RC5

## Slide 18: Key Expansion

## Slide 19: The magic constants
In key expansion, magic constants are used
 Pw = Odd((e - 2)2w); e=2.718281828…. (base of natural logarithms)
 Qw = Odd(( - 1)2w);=1.618033988…. (golden ratio = (1+sqr(5))/2)
  Odd(x): odd integer nearest to x
 Example
w 16 | 32 | 64
Pw B7E1 Qw 9E37 | B7E15163 9E3779B9 | B7E151628AED2A6B 9E3779B97F4A7C15

## Slide 20: Step-1: Convert secret key bytes to words
Copy the Key into new array L of Words with size equal c Any unfilled byte positions of L are zeroed
In case b = c = 0 we reset c =1 and set L[0] = 0

## Slide 21: Step-2: Initialize sub key array S
create an expanded key table, S[0...t-1]

has t entries, t = 2(r + 1) w-bit words
Initialize array S
S[0] = Pw;
for i = 1 to t - 1 do
S[i] = S[i - 1] + Qw;

## Slide 22: Step-3: Mix the secret key into sub key array S
Mix the secret key into table, S
i = j = 0; A = B = 0;
do 3 * max(t, c) | times: |  | 
A = S[i] = | (S[i] + A | + B) <<< 3; | 
B = L[j] = | (L[j] + A | + B) <<< (A + | B);
i = | (i + | 1) mod(t);
j = | (j + | 1) mod(c);

## Slide 23: Key Expansion Algorithm

## Slide 24: The security of RC5
Exhaustive Search
Differential cryptanalysis
Linear cryptanalysis
Timing Attacks

## Slide 25: Exhaustive Search
RC5-32/r/b allows
  a maximum of 2040 secret key bits
  a maximum of 25(2r + 2) expanded key table bits
Choosing large values for r and b can prevent exhaustive attacks

## Slide 26: Differential cryptanalysis

It has a quite evolutionary effect on the design and analysis of block ciphers
The basic Idea
Two plaint text are chose with a certain difference P` (The difference here is measured by xor but for other cipher alternative measure may be applied)
The two plaintexts are enciphered to give two cipher texts such that their difference C`
Such a pair (P` , C`) is called a characteristic
Depending on the cipher and the analysis the behavior of this characteristics can be useful in deriving certain bit of the key


## Slide 27: Linear cryptanalysis
Introduced By Matsui.
The basic idea is
  to find relations among certain bits of plaintext, cipher text and key
  Such as relation is called linear approximation which can be used to obtain information about the key
Becomes impractical for r > 6

## Slide 28: Differential and Linear attack

## Slide 29: Conclusion
Provides good security against the four main attacks
Simple encryption/decryption algorithms
RC5 is relatively is still under scrutiny by other cryptanalysis attack